# Drive with analog reference
Upon request, the servo amplifier can be controlled via analog input, also it is fitted with an output “line driver” 5V type encoder emulation.
The resolution of the emulated encoder is the same as the main motor encoder. You can't set an encoder emulation with a variable number of pulses / revolutions. It is possible to find a comprehensive overview of the device connections in paragraph 6. The connectors to be used for driving in analog are C9: analog input; C7 encoder emulation and C5: inputs and outputs.
## Analog Input
Analog-In 1 Input (terminal C9/1-4), differential analog input 12bit
Differentials input voltage of max. ± 10 V
Connect the controller (PLC or NC) as following indicated

analog_1.jpg

analog_2.jpg
## Example using a potentiometer
If you want to drive the servo amplifier by a potentiometer and you do not have a ± 10V dual voltage power supply, the voltage can be derived using the following circuitry. The first diagram shows how to drive the motor with a voltage from 0 to 10V, the second one with a voltage from 0 to-10V.

pot_1.jpg
## Encoder Emulation
With the “analog” option the connector C7 provides the emulation of the motor encoder. The C8 connector on the contrary will not mount.
The emulated encoder output is a 5V opto line-driver type. The emulated encoder resolution is fixed and it is the same as the motor main
encoder (default 2048ppr)

enc.jpg