# CanOPEN PDO Example
The mode of operation is mapped at index 0x6060 subindex 0 with size of 1 byte. For example: Profile position is 1, Profile velocity is 3, Torque profile is 4, Interpolated position is 7.
The communication is with DS402 Profile on CiA 301 (CAN in Automation). Reference: https://en.wikipedia.org/wiki/CANopen
PDOs must be transmitted and received at every Sync, COB ID = 0x80. Master can access the parameter inside the slave using SDO read and write.
See here: https://www.nilab.at/dokuwiki/doku.php?id=mbd_servo_drive:registers|
## How to program using SDO write - Position control - Interpolated position
### Configuration of PDO from Slave to Master
COB ID	D0	D1	D2	D3	D4	D5	D6	D7	Comment
0x600+(nodeid)	0x23	0x00	0x1A	0x01	0x20	0x00	0x64	0x60	Position actual value
0x600+(nodeid)	0x23	0x00	0x1A	0x02	0x10	0x00	0x41	0x60	Status word
0x600+(nodeid)	0x23	0x00	0x1A	0x03	0x08	0x00	0x61	0x60	Mode of operation display

### Configuration of PDO from Master to Slave
COB ID	D0	D1	D2	D3	D4	D5	D6	D7	Comment
0x600+(nodeid)	0x23	0x00	0x16	0x01	0x20	0x00	0xC1	0x60	Interpolated data record
0x600+(nodeid)	0x23	0x00	0x16	0x02	0x10	0x00	0x40	0x60	Control word
0x600+(nodeid)	0x23	0x00	0x16	0x03	0x08	0x00	0x60	0x60	Mode of operation

## How to program using SDO write - Torque control
### Configuration of PDO from Slave to Master
COB ID	D0	D1	D2	D3	D4	D5	D6	D7	Comment
0x600+(nodeid)	0x23	0x00	0x1A	0x01	0x10	0x00	0x77	0x60	Torque actual value
0x600+(nodeid)	0x23	0x00	0x1A	0x02	0x10	0x00	0x41	0x60	Status word
0x600+(nodeid)	0x23	0x00	0x1A	0x03	0x08	0x00	0x61	0x60	Mode of operation display

### Configuration of PDO from Master to Slave
COB ID	D0	D1	D2	D3	D4	D5	D6	D7	Comment
0x600+(nodeid)	0x23	0x00	0x16	0x01	0x10	0x00	0x71	0x60	Target Torque
0x600+(nodeid)	0x23	0x00	0x16	0x02	0x10	0x00	0x40	0x60	Control word
0x600+(nodeid)	0x23	0x00	0x16	0x03	0x08	0x00	0x60	0x60	Mode of operation

Additional parameter are 0x6087 ⇒ Torque Slope and 0x6088 ⇒ Torque profile type (0 = Linear ramp)
## STATUS WORD Register
BIT Number	Description	Mode of operation
11
12		Interpolated positioning
12		Profile velocity
13		Profile velocity
12		Homing
13		Homing
12		Profile positioning
13		Profile positioning

## CONTROL WORD Register
BIT Number	Description	Mode of operation

1
2
3
4		Homing
4		Interpolated positiong
4		Profile positioning
5		Profile positioning
6		Profile positioning
7
8

## DS402 State Machine

### Enabling the drive
SERVO-ON: is procedure that Master should read Statusword from driver and send corresponded Controlword (command) to driver to make it change to final state, Operation Enable. The common SERVO-ON path in CiA 402 state machine is: (1) → (2) → (3) → (4) or (13) → (14) → (15) → (2) → (3) → (4)
### Disabling the drive
SERVO-OFF: is procedure to switch off servo drive, that is moving its state to 'Switch On Disabled' state. The shorted path is transition (9) in which Master send Controlword of 0 to an operating driver.
## EDS (CanOPEN) and XML (ETHERCAT) files
EDS File: https://www.nilab.at/download/mbd-tbs1-eds-file/?wpdmdl=2134&refresh=637351b05ed9d1668501936
XML File: https://www.nilab.at/download/mbd-tbs1-ethercat-eds-file/?wpdmdl=3335&refresh=637351b0868111668501936