# MODBUS RTU
MBD servo drive implements Modbus RTU protocol on a RS232 serial point to point communication interface.
## Available functions
Function name	Function code
Read Holding Register	0x03
Write Single Register	0x06
Write Multiple Registers	0x10

## Modbus register areas
Parameter type	MODBUS address
Servo parameter	0x00 to 0x3FF
Input variables	0x1000 to 0x103F
Output variables	0x1200 to 0x123F

## Basic command
Enabling, disable and set the speed
Command	Address	Data Write	Unit	NOTE
Opmode	0x0010	2	-	2 = digital speed
Enabling	0x1000	bit 0 = 1	-
Disabling	0x1000	bit 0 = 0	-
Speed setpoint	0x1026	xxxx	RPM

Reading the status and the current
Command	Address	Data Write	Unit	NOTE
Enabling OK	0x1200	Bit 0 = 1	-	if enabled bit 0 is set to 1 otherwise is set to 0
Read speed	0x1218	xxxx	-
Read Q current	0x1210	xxxx	Amper x 10

## Input Variable table

input_param.jpg
## Output Variable Table

var_out.jpg